## Slide 1: Water Quality Analysis
We are team
Fourcast
Y. Deekshitha
2022101009​
Renu Sree Vyshnavi
2022101035
Varshitha 2022101054​
R. Shaanal
2022102071​
Notes: Introducing Ourselves. We are team Fourcast doing the project the Water Quality Analysis,

## Slide 2: Agenda
Water quality specifications
Data collection
Water quality Analysis of:
  River water
  Ground water
  Marine/Creeks
Water Quality Index
Geo-Website-Demo
Model assessments
Future Predictions
Dashboard Demo
Mini Web-Demo-2
Notes: This is the plan we followed in the presentation

## Slide 3: What is water quality?
Water quality is defined by the standards set for the parameters of measuring water which are good for consuming or using by an average person.
Water quality refers to the condition of water based on its chemical, physical, and biological characteristics, and its suitability for various uses and the health of aquatic ecosystems
Notes: Coming to water quality: It refers to the condition of water based on its chemical, physical and biological data which allows it to be suitable for various uses and health of aquatic life.

## Slide 4: Water quality specifications
References:
Primary Water Quality Criteria
Designated Best Use Water Quality Criteria
BIS Drinking Water — Specification
Coastal Water Standards
The above references are the documents specifying the set standards for water analysis of rivers, groundwater and costal areas.
Let’s analyze more about these as we dive into the definitions of the water we are dealing with.
Notes: After referring to these sites for understanding the specifics of water quality, we calculated the water quality Index. Before going more into the water quality index, we explored the different types and the characteristics of the data we collected.

## Slide 5: Water body Types we are looking into…
India has many water bodies, rivers, their tributaries, canals, drains, seas, creeks, groundwater, etc.,
Marine:
Rivers:
link_to_river_pic
Canals:
link_to_canal_pic
Creeks:
link_to_creek_pic
Ground water:
link_to_marine_pic
Notes: The data we used majorly consists of River, Groundwater and Marine water. Then Sea water, beaches, creeks, canals, STPs, WTPs, that is treatment plants outlets, were also considered.

## Slide 6: Water Quality Criteria
A: Drinking Water
Drinking water source after conventional treatment and disinfection
D: Aquatic Life
Propagation of Wild life and Fisheries
C: Drinking Water
E: Agriculture and Industrial
Total Coliforms Organism MPN/100ml shall be 50 or less
Drinking Water Source without conventional treatment but after disinfection
pH between 6.5 and 8.5
Dissolved Oxygen 6mg/l or more
Biochemical Oxygen Demand 5 days 20C 2mg/l or less
Outdoor bathing water (Organised)
pH between 6.5 and 8.5
Dissolved Oxygen 5mg/l or more
Biochemical Oxygen Demand 5 days 20C 3mg/l or less
Total Coliforms Organism MPN/100ml shall be 5000 or less
pH between 6 to 9
Dissolved Oxygen 4mg/l or more
Biochemical Oxygen Demand 5 days 20C 3mg/l or less
B: Outdoor bathing
-
pH between 6.5 to 8.5
Electrical Conductivity at 25C micro mhos/cm Max.2250
Sodium absorption Ratio Max. 26
Boron Max. 2mg/l
Total Coliforms Organism MPN/100ml shall be 500 or less
Irrigation, Industrial Cooling, Controlled Waste disposal
Dissolved Oxygen 4mg/l or more
Free Ammonia (as N) 1.2 mg/l or less
pH between 6.0 and 8.5
From WHO guidelines, BIS Standards and CPCB guidelines
Notes: This is the criteria for good quality water for different categories: Drinking water,

## Slide 7: Coliform Bacteria
We are using Fecal Coliform and Total Coliform values to determine water quality. That is, they act as one of the major contributors to water quality index along with Dissolved oxygen and Biological oxygen Demand.
Total coliforms include bacteria that are found in the soil, in water that has been influenced by surface water, and in human or animal waste. Fecal coliforms are the group of the total coliforms that are considered to be present specifically in the gut and feces of warm-blooded animals

## Slide 8: Oxygen
As much as both Dissolved Oxygen and Biological Oxygen Demand are both about oxygen, they are negatively correlated.
Biological oxygen demand (BOD) is a measure of how much oxygen is required to break down organic matter in water.
Dissolved oxygen (DO) is the amount of oxygen gas dissolved in water.

## Slide 9: pH
It is a logarithmic scale used to specify the acidity or basicity of the water.
For water bodies like rivers, seas and groundwater table, a pH range of 6.5 to 8.5 is considered good quality.

## Slide 10: Data Collection
We collected data from the CPCB website.
There are other datasets from Kaggle but we found the official website to have more data.
Even though the data was better organized in this website as per the years, they were all in pdfs with different columns each year. This added to the challenges faced during data collection and extraction.

## Slide 11: Data Attributes
Geo-Attributes | WQI-attributes | WQI-attributes | Other columns which we did not consider
Station Code | pH - min, max | NN - min, max Nitrates and Nitrites | Temperature
State | BOD - min, max Biological Oxygen Demand | DO - min, max Dissolved Oxygen | Location
Latitude | FC - min, max Fecal Coliform |  | 
Longitude | TC - min, max Total Coliform |  | Conductivity

## Slide 12: Data Pre-Processing
We collected the coordinates information from a separate pdf from the same site and it was related to the station code. To construct geological analysis maps.
Removing unnecessary columns like LOCATION.
Removing missing value columns or replacing with mean/median values ( Filling missing values with station-specific means )

## Slide 13: Data Inconsistencies
We faced a lot of problems with creating a consistent analysis or prediction,
The data had mismatching columns over different years.
We observed inconsistency in collecting the data from the same station at all years.
We also observed a lot of missing values.
There were stations with no data collected but in the file.
The names of the states were not common, i.e., they same state/union territory had 2 names. Ex.: “DELHI”, “CPCB, DELHI”
Notes: We had problems

## Slide 14: Visualisation of stations used by CPCB using QGIS

## Slide 15
Geo-Website

## Slide 17: Web-Demo

## Slide 18
Data Analysis of Water Quality Parameters, Water body type-wise and Attribute-wise
Shown in Code:………..

## Slide 19
Correlation of Water Quality Parameters, Water body type-wise
Shown in Code:………..

## Slide 20: Water Quality Index
Weights | Rivers | Groundwater | Marine
Dissolved Oxygen | 0.26 | - | 0.25
Total Coliform | 0.20 | 0.20 | 0.10
Fecal Coliform | 0.17 | 0.17 | 0.20
Biological Oxygen Demand | 0.22 | 0.22 | 0.20
pH range | 0.15 | 0.15 | 0.15
Nitrates and Nitrites | - | 0.28 | 0.10
If the given data for a station has all attributes satisfying the necessary conditions, as discussed before, we give each attribute a score of how perfect it is, 100 being the best score.
Finally, give weights for each attribute and sum them to get the water quality index (WQI).
The weights are given as shown in the table.
Notes: This slide shows how we calculate the Water Quality Index using selected parameters like pH, BOD, nitrate, fecal coliform, and total coliform. Each parameter is first normalized based on standard quality ranges. We then assign weights to reflect their relative importance to water quality. Finally, a weighted average is used to compute the overall WQI. These are the weights for Rivers, Groundwater, Marine respectively. To question why we chose them, we chose them following the CPCB guidelines and WHO and BIS standards of water quality. The references for which were added before.

## Slide 21: WQI Analysis
Improvements due to COVID-19
Quality ranges per year with Standard deviation (1) and Average (2)

## Slide 22: Dependency
This graph shows how each attribute relatively contributes to WQI.

## Slide 23: Correlation Map
Everything here is negatively correlated with WQI due to the upper bound constraint except for Dissolved Oxygen which has a lower bound constraint.
Notes: DO >= 5mg/l while

## Slide 24
Dashboard
For
Future
Predictions
Notes: To analyze.
Predicting future data. Testing with 2023/2022 wqi for analysis. Proves RF and ARIMA to be better models over basic linear regression. Showing the pics while explaining this. Dashboard demo.

## Slide 25: Data Preparation
Reads multiple CSV files from a directory (one per year)
Extracts the year from each filename and adds it as a column
Handles potential encoding issues by trying multiple encodings (utf-8, latin1)
Combines all data into a single Data Frame for analysis
Filters data for a specific station
Splits data into training (years before validation_year) and validation sets.
Creates lag features (previous year's WQI value) for time series modeling

## Slide 26: Linear Regression
What it does: It fits a straight line (linear relationship) between the input features and the output (target) variable. The model tries to minimize the error between predicted and actual values using least squares
Implementation: LinearRegression() from scikit-learn
Features used: Year and previous year's WQI value
Strengths: Simple, interpretable, works well for linear trends
Time series application: The lagged feature (previous year's WQI) introduces time dependence

## Slide 27: Random Forest Regressor
What it does: An ensemble learning method that builds a large number of decision trees during training and outputs the average prediction from all the trees. Each tree is trained on a random subset of the data and features (bagging).
Implementation: RandomForestRegressor(n_estimators=100) from scikit-learn
Features used: Same as linear regression (year and previous year's WQI)
Strengths: Can capture non-linear relationships, robust to outliers
Time series application: Like linear regression, uses lagged features for time dependency

## Slide 28: ARIMA (AutoRegressive Integrated Moving Average)
What it does: A classical statistical model specifically designed for time series. It combines three components:
    AutoRegressive (AR): Past values are used to predict the current value.
    Integrated (I): Differencing is used to make the series stationary.
    Moving Average (MA): Past prediction errors are used to improve accuracy.
Implementation: ARIMA(order=(1,1,1)) from statsmodels
Parameters: p=1 (autoregressive order), d=1 (differencing), q=1 (moving average order)
Strengths: Specialized for time series, captures trends and seasonality
Time series application: Built specifically for sequential data prediction

## Slide 29: Validation and Future Predictions
Validation:
Uses data from validation_year (default 2023) to test model performance.
Calculates error metrics (absolute error and percentage error) for each model.
Helps determine which model is most accurate for each station.
Future Predictions:
Makes predictions for future years (default 3 years ahead).
Uses an iterative approach where each prediction becomes input for the next prediction.

## Slide 34: Prediction Dashboard Demo

## Slide 35: Website-Demo-2 mini-chatbot just for definitions for the water attributes

## Slide 36
💬 Chat-Based Q&A on water quality topics
🧠 Covers Parameters like pH, BOD, DO, turbidity, etc.
📊 Tables & Ranges for values and standards
🧂 Fun Facts & Jokes based on water bodies included for engagement
Used openrouter.ai API

## Slide 37: Thank You !